## Slide 1
Lipetsk city, Lipetsk region, the RF
Project leader:
Candidate of Engineering Sciences, Director General of “System48 Scientific Production Enterprise”
Sergei Titov
Development of manufacturing technique and innovative equipment for axisymmetric induction heating of metalware with the discrete cross-section area

## Slide 2
Manufacturing of continuous power efficient equipment that ensures the axisymmetric heating to the given depth for the heat treatment of ball-shaped products without oxidation and decarburization is extremely urgent for a number of productive industries, in particular in the mass productions of grinding bodies for ore mining and processing mills and cement plants, frictionless bearing balls and valves in the hydraulic systems, including high-wear-resistant balls in working barrel back pressure valves for oil production, etc.
The induction method with direct and high speed (seconds – fractions of a second) electric energy to heat energy conversion which is notable for the simplicity in control of temperature and depth of heat meets best of all this set of heating characteristics required by the industry. It permits the optimal combination of high surface hardness of products (back-to-back endurance) with rather yielding core (shear strength) after quenching and tempering.
However, despite of all the known advantages of this method nowadays its applicability with the required axial symmetry of heating is limited in the world mainly by the products of continuous section or similar to it.
The project under development resolves the issue raised.
Introduction

## Slide 3
PROJECT TASK
Commercialization of the innovative technology which allows for the increased surface hardness, strength, wear resistance of metal balls with their cost reduction at the same time
Product - Technology

## Slide 4
CONSUMERS OF METAL BALLS
Iron-ore concentration in the metallurgy (grinding balls in ball mills)
The building sector: the production of silicates, cement
(Clinker grinding with grinding balls in ball mills)
Bearing balls
Oil production
(working barrel back pressure valves )
Heat treatment
High-tech methods to give the desired properties to spherical surfaces by means of symmetrical thermal diffusion alloying (chromium, titanium, boron etc.)

## Slide 5
The main consumer of grinding balls in Russia is an iron-ore sector, deliveries of which occupy 40% of the market
The pattern of consumption of grinding balls
in the Russian market (2018, %)
1. Apatites, uranium, ores for the production of refractory products, etc.
Source: NLMK Group (RZhD database), Rosstat, data from companies and industry associations, the analysis made by A.T. Kearney
Mineral resource industry
(ore reduction) 85%
Energy sector
(breakage of coal for coal-fired thermal power plant) 2%
Cement industry
(Clinker grinding) 13%
1
Coal
Cement
Iron
Copper und nickel
Gold
Aluminium
Other ores1
2%
13%
40%
17%
17%
3%
2
3
NLMK Group consumes ~9% of grinding balls in the RF market
Metalloinvest
NLMK Group
Other (iron)
14%
10%
16%
EVRAZ
Severstal
7%
4%
Norilsk Nickel
UMMC
Other (copper und nickel)
9%
2%
PATTERN OF CONSUMPTION OF GRINDING BALLS IN THE RF

## Slide 6
Total Cost of Ownership of balls
1.2 Consumption record of balls 1%
2.Price of balls 41%
2.2 Suppliers
1.Consumption of balls 51%
1.1 Quality of balls 50%
1.1.5 Geometric ball shape
1.1.6 Ball diameter
1.1.1 Chemical composition
1.1.4 Quality of surface
1.1.2 Presence of internal defects
2.2.1 Incoming control
1.1.3 Volume hardness
3. Power consumption for grinding 8%
3.1 Electricity metering
TCO* FACTOR ANALYSIS OF GRINDING BALLS**
*- Total Cost of Ownership
** - The used tool is Ishikawa diagram (It is often called “a fish bone” in the Russian literature)

## Slide 7
PROBLEM OF HIGH TOTAL COST OF OWNERSHIP (TCO) OF GRINDING BALLS (ANALYTICS)
Consumption of balls 51 %
(poor quality of balls)
Price of balls 41 %
(high prime cost of balls)
Power consumption for grinding 8 %
TCO of grinding balls in “SGOK” ОАО
Annual parameters | “SGOK” ОАО | The RF
Consumption, th. tonnes | 47.9 | 609
Costs, mln. Rub. | 1,916 | 24,360
ТСО, mln. Rub. | 4,673 | It depends on the branch
Loss of profit by 1 % of TCO reduction, mln. Rub. | 46,7 | It depends on the branch
Ore processing volumes and the consumption rate of grinding bodies
Ore processing volume, mln. t
Ore concentrate production volume , mln. t
Rate of use of grinding bodies per one tonne of the processed ore, kg/t
In the course of further field development it is expected to have a decrease in the concentrate specific yield from a tonne of in-process ore
Consumption volume of grinding bodies, th. tonnes a year
Grinding balls, D 40 mm
Grinding balls, D 60 mm
Grinding balls, D 100 mm
The rate of use of grinding bodies per one tonne of in-process ore will keep on growing1 because of the gradual decline in ore preparation characteristics
1. With disregard for a possible effect from the change of a supplier and/or a type of grinding bodies
Source: SGOK, the analysis made by A.T. Kearney
Taking into account a number of large-scale projects in copper, iron and gold a market growth of grinding bodies can be expected by 2020.

## Slide 8
Historical price behaviour* for grinding balls,
th. Rub. / t
Source: SGOK of “NLMK” PAO, the analysis made by A.T. Kearney
In 2015-2017 the price behaviour of grinding balls reflected the change of prices for steel with a time lag of 3-6 months
Steel balls, D 100 mm, hardness of group 3
Steel balls, D 60 mm, hardness of groups 2-3
Steel balls, D 60 mm, hardness of groups 2-3
Quoted prices of Billet FOB Black & Baltic Sea ports
export
Apart from the beginning of 2015 cast-iron balls were consistently cheaper than the steel ones
by ~3,500-5,500 Rub/t
PRICE BEHAVIOUR OF GRINDING BALLS , MARKET SIZE
The RF market, bln. Rub.
The world market, bln. Rub.
PAM
TAM
SAM
SOM
PAM
TAM
SAM
SOM
20,1
23,7
108,2
125,8
?**
**- it is not planned to enter the world market at the first stage
0,73
2,1
37,3
*- the prices correlate with the prices for raw materials (metal wheel)

## Slide 9
The global leader Arrium owns ~30% of the market, but it only operates in the markets of North and South America and Australia
There are four leading global players which operate with the works in different regions of the world:
  Arrium1 : 7 works in South and North America, Australia and Indonesia, the global market leader in facility size (29% of the market)
  Magotteaux : 13 works in Europe, North and South America, Asia and South Africa
  AIA Engineering2 : production in India and active supplies to South and North America, Australia, South Africa and Europe
  ME Elecmetal : 5 works in South and North America
78 regional producers which considerably differ in the production output and the skill level
  GIS leading producers: EVRAZ, METINVEST and UzMetKombinat (Uzbeksteel) make the top 10 of the largest world producers according to the facility size
World market structure of grinding balls
Names before 2012: Moly-Cop and OneSteel
Trade mark in export markets: Vega
Source: Arrium, SPARK, KOMPASS, Capital IQ, the analysis made by A.T. Kearney
Size of production facilities,
th. t
Other
producers 1697
Donhad 140
4%
Gerdau 140
ME Elecmetal 154
UzMetKombinat 170
METINVEST 170
3%
AIAE (Vega) 200
3%
EVRAZ 250
6%
Magotteaux 308
7%
Arrium1 1290
29%
Total = ~4,500 th. t
PRODUCERS OF METAL BALLS IN THE WORLD
(TRADITIONAL HEATING TECHNOLOGY FOR HEAT TREATMENT)

## Slide 10
GEOGRAPHY OF PRODUCERS AND CONSUMERS OF GRINDING BALLS IN THE WORLD
The global market of grinding balls makes up ~3 bln. t. and grows by 4-5% a year, but its facilities are only ~70% utilized
Regional balances of grinding bodies
(2017, th.t)
The world market size of grinding bodies makes up ~2.9 bln.t., 90% of which is consumed by the mining sector
The key regions of consumption are GIS, South and North Americas, China and Australasia
In 2014-2017 the annual market growth rates made up 4-5% a year
The production of grinding bodies is mainly concentrated in the regions of their consumption; the total capacity utilization makes up ~70%
India and China are the largest exporters of grinding bodies, exporting respectively 60 and 30 th. t a year

## Slide 11
снижение качества термообработки
METAL STRUCTURE BEFORE TREATMENT
METAL STRUCTURE AFTER TREATMENT
HEATING IN GAS FURNACES or
RESISTANCE FURNACES (heating elements)
Induction heating HFC!
QUALITY OF HEAT TREATMENT MEANS QUALITY OF BALLS
TRADITIONAL APPROACH
PROPOSED APPROACH

## Slide 12
INNOVATION HEATING TECHNOLOGY FOR HEAT TREATMENT
A round workpiece
The cross-rolling mill
The conveyor
The proposed induction plant
The hardening plant
Heat-treatment cell
It is possible to integrate into the existing processing lines of manufacturing companies!
INPUT – STAGE 1
OUTPUT
THE AXISYMMETRICAL BALL ROTATION IN THE ENVIRONMENT WITH ELECTROMAGNETIC FIELD
CONTROL OF
TEMPERATURE AND
DEPTH OF HEATING
MINIMUM VIABLE PRODUCT (MVP)

## Slide 13
ADDITIONAL COST OF INNOVATION TO THE CONSUMER
The application of the proposed technology makes it possible to have a unique double effect: improvement in quality of grinding balls and cutting of their production costs at the same time, what will finally permit the ТСО of grinding balls to be considerably reduced
Increase of the plant coefficient of efficiency (direct heating of the ball material with electromagnetic field energy)
Surface heating of the ball to the given depth
(energy is not consumed for the core heating of the product)
High-speed heating (there is no need to consume energy for hours)
AXISYMMETRIC heating of the ball material is possible to the given depth
The effect of SHEAR STRENGTH is achieved: it is possible to get a yielding core of the ball
It is possible to ensure ZERO OXIDATION AND DECARBURIZATION as a result of high heating rate
Increase of service
life up to
1.6 times
cutting of the production costs by
7.2 %
TCO reduction of grinding balls by 23.3 %
(about 40 euro cents per tonne of processed ore)

## Slide 14: COMPARISON OF THE PRODUCT TECHNICAL AND ECONOMIC CHARACTERISTICS TO THE WORLD COMPETITORS

## Slide 15
PROJECT BUSINESS MODEL*
KEY PARTNERS
KEY ACTIVITIES
KEY RESOURCES
VALUE PROPOSITIONS
CHANNELS
COST STRUCTURE
REVENUE STREAMS
Iron and steel enterprises (including the product dealers): deliveries of round workpieces)
Human resources;
2) Intellectual property (patents, innovative solutions): intangible assets;
3) Material resources (equipment (HFC inductors), a building (to install the production line), an office, tools and components and etc.);
4) Financial resources (physical cash and non-cash money);
5) Raw materials.
Production of metal balls of high quality with TCO reduction for the customer
Additional income of the enterprises that consume the output product as a result of TCO reduction of the delivered metal balls
Sales of licenses to manufacture and run the equipment under development;
Sales of the equipment under development;
Disposal of metal balls.
Fixed costs (salaries and wages of the employees, rent price of the premises, depreciation charges, contributions to different social funds and etc.);
Raw materials and energy;
Customer acquisition costs.
It is planed to arrange direct and indirect sales of the product to the customers
1) Personal support;
2) Generating of joint value proposition
CUSTOMER RELATIONSHIPS
1) Mining and processing integrated plants;
2) Building sector (production of silicates, cement);
3) Ball bearing sector (frictionless bearing balls);
4) Oil production (working barrel back pressure valves);
5) Heat treatment (High-tech methods to give the desired properties to spherical surfaces by means of symmetrical thermal diffusion alloying (chromium, titanium, boron etc.)
CUSTOMER SEGMENTS
* - in compliance with the methods of А. Osterwalder

## Slide 16
COMMERCIALIZATION PLAN FOR PROJECT OUTPUT
R&D
Pilot lot production of metal balls
Disposal of the pilot lot of balls to the consumer
Remarks made by the first consumer
Updating of R&D results
Yes
No
Pilot plant
Production
1
1
Pilot lot production of metal balls for “Severstal” PAO*
Disposal of the pilot lot of balls to “Severstal” PAO*
Remarks made by “Severstal” PAO*
Yes
No
Updating of the pilot plant
Arranging supplies of metal balls inside “Severstal” PAO*
2
2
* - or another iron and steel company, for example, «NLMK» PAO
Complete satisfaction of demand of “Severstal” PAO* in quality of metal balls
Production distribution to integrated iron-and-steel works from other RF regions
Diversification of market outlets
3
3
Entrance to the foreign market outlets of the product
«Exit» strategy implementation
(sale of technology to one of the powerful players in the market)
Cost efficiency indexes of project implementation (production) |  |  |  |  | 
Investment stage, years | Project cycle, years | NPV, mln. euro | IRR, % | nок, years | ROI
2 | 5 | 17,4 | 81.3 | 2.7 | 3.8

## Slide 17
PROJECT TEAM
Project leader as Director
Manager of “marketing” department
Senior scientist
Chief engineer
Accountant
Doctor of Engineering Science, full professor, Head of the Department of Electric Drives at FSBEI HPO “Lipetsk State Technical University". He is experienced in commercialization of 9 inventions. He participated in R&D as an academic adviser and an inventor of their underlying ideas. He is a full member of the International Academy of Natural Science and the Russian Academy of Quality Problems.
Candidate of Engineering Sciences, an engineer at the Process Flow Automation Department of “Novolipetski metallurgicheski kombinat (NLMK)” PAO. He has a programming skill with such industrial controllers as Siemens Simatic Series 200/300/400/TDC, Schneider Premium/Quantum in the languages standardized by IEC 61131-3. He developed projects for the human-computer interface tools based on Siemens WinCC/WinCC Flexible and Schneider Electric Citect systems. He has an experience in design and adjustment of electrical drives of different manufacturers (Siemens: Simoreg, Simovert, Micromaster, Sinamics, Schneider Electric: Altivar 31,71, Emerson Unidrive SP, Mitsubishi FR, Baumuller bMax 4400).
The project leader is a Candidate of Engineering Sciences; an inventor of the project idea; a many-time contestant and prize winner of prestigious innovation competitions. He got a workout under the specialists’ supervision from McKincey and Company (in particular in Germany). He has raised investment for the project at the total amount of about 8 mln. Rub., including from the non-budget sources. He has a successful collaborative experience with the regional authorities.
Candidate of Historical Sciences,
He has a management experience in a joint Russian-American project; he is a leader of projects in the development of electronic interaction system between the state and the society (the system of Multifunctional centres in Lipetsk region); an initiator and a leader of a number of IT projects for the regional authorities; he provided two electoral campaigns of Lipetsk city head with the sociological support.

## Slide 18
Steps for 2 months 2019
The examination was undergone
Sk
The funds were obtained
Sk
on April 10
on April 29
on May 20
The international patent process under the PCT was started
“System48 Scientific Production Enterprise” Company Limited (ООО), room 2, building A, 13 ul.Pushkina, 398001, Lipetsk city,
Tel.: +7 (904) 690 2601, e-mail: main@system48.ru, PSRN: 1164827055645, TIN/RVC: 4826123123/482601001, Settlement account No.: 40702810902930001612 set up in “ALFA-BANK” AO, Moscow city branch, TIN: 7728168971, PSRN: 1027700067328, RCBIC: 044525593, Loro account: 30101810200000000593